The system contains:
- SAM3-P256 development board
- 2.4” TFT SPI 240x320 LCD module. (Touch control with XPT2046 IC, and SD card SPI connector.

Port	Function	Display function (ILI 9341)	Touch control function (XPT2046)	SD card connector SPI port
3.3 V	+ 3.3 V	VCC	VCC	VCC
GND	GND	GND	GND	GND
PA11 (NPCS0)	Out	CS	-	-
RST	Out	Reset	-	-
PA1	Out	D/C	-	-
PA13 (MOSI)	Out	SDI (MOSI)	T_DIN	-
PA14 (SPCK)	Out	SCK	T_CLK	-
PA12 (MISO)	In	SDO (MISO)	T_DO	-
3.3 V	+ 3.3 V	LED	-	-
PA0	In	-	T_IRQ	-
PA31 (NPCS1)	Out	-	T_CS	-
PA10 (NPCS2)	Out	-	-	SD_CS

Connecting to OLIMEX SAM2-P256 board.